## Slide 1: Department of Informatics Networks and Distributed Systems (ND) group
How to Control a TCP: Minimally-Invasive Congestion Management for Datacenters
ICNC 2019, Honolulu
18. 02. 2019
Safiqul Islam, Michael Welzl, Stein Gjessing

## Slide 2: What is this about?
In multitenant datacenter, the guest OSes of clients may be diverse and utilize an Internet-like mix of old and new TCP congestion control implementations
This may put some users at a disadvantage, depending on how aggressively their congestion control probes for capacity
  unfair users may have an incentive to obtain a larger share of the capacity by opening multiple TCP connections .unsatisfied customers!

## Slide 3: What is this about?
Sending rate of two VMs, with 1 flow in VM1 and 1 to 4 flows in VM2

## Slide 4: Prior work
Mechanisms such as Seawall [1], VCC [3] and AC/DC [2] successfully achieve this sender-side control by running dedicated congestion control algorithms as part of the hypervisor infrastructure
  But: how should the new algorithm that is running as part of the hypervisor communicate with the the guest OS?
Seawall alone takes care of the congestion control
  CC implementations need to defer all congestion control decisions to the hypervisor (asking for allowance before sending a packet )_
  the sender and receiver side are altered, and bits from the header are re-purposed to implement the necessary signaling
[1] A. Shieh, S. Kandula, A. Greenberg, C. Kim, and B. Saha, “Sharing the data center network,” in Proc. of NSDI, 2011.
[2] K. He, E. Rozner, K. Agarwal, Y. J. Gu, W. Felter, J. Carter, and A. Akella, “AC/DC TCP: Virtual congestion control enforcement for datacenter networks,” in Proc. of SIGCOMM, 2016
[3] B. Cronkite-Ratcliff, A. Bergman, S. Vargaftik, M. Ravi, N. McKeown, I. Abraham, and I. Keslassy, “Virtualized congestion control,” in Proc. of the ACM SIGCOMM, 2016.

## Slide 5: Prior work
AC/DC do not require updating the guest OS at all,
  which is a significant advantage: it does not require cooperation of tenants to update the OS (if they do bring their own OS),
    which reduces burden and allows to enforce cooperative behavior
Changes the receive window (rwnd) as a means to control TCP’s behavior
  A sender can therefore only increase the sending rate as quickly as the TCP implementation inside the guest OS allows

## Slide 6: Prior work on congestion management
Datacenter capacity management
  Access is controlled at the edges (EyeQ), FairCloud (per flow queues at the switches), Seawall, AC/DC, VCC
Single-path congestion control coupling
  By sharing a number of state variables
Multiplexing
  By merging application layer datastreams onto a single transport layer connection
Multi-path congestion control coupling
  MPTCP’s coupling assumes that flows could take a different path, and ideally also traverse different bottlenecks

## Slide 7: Our contribution
A new interface (ctrlTCP_int) to communicate between TCP in the guest OS and a hypervisor.
  A set of TCP connections are controlled via this interface
Extended our ctrlTCP algorithm that emulates the behavior of a single TCP congestion controller
  Supports prioritization (for practical management of both inter- and intra-VM capacity allocation)
Show the efficacy of our solution using both ns2 and FreeBSD

## Slide 8: CtrlTCP interface
A middle ground can be found by keeping the guest OS congestion control intact, yet allowing a controlling entity to overrule its decisions
ctrlTCP operates strictly on the control path:
  communicates signals cc in the guest OS and the hypervisor
    not needed to even examine or count the outgoing or incoming packets

## Slide 9: CtrlTCP algorithm
Each TCP session communicates with an entity that we call a Coupled Congestion Controller (CCC)
  typically makes decisions that combine the collected knowledge that it receives from all TCP instances that talk to it - thereby “coupling” them in some way
  A CCC can operate in a hypervisor or in an OS
S. Islam, M. Welzl, H. Kristian, D. Hayes, G. Armitage, and S. Gjessing, “ctrlTCP, reducing latency through coupled heterogeneous multi-flow TCP congestion control,” IEEE GI 2018

## Slide 10: ctrlTCP
TCP Session
CCC
register(c, p, cwnd, sshtresh)
accept (cwnd, ssthresh)
Initialization:
First conn:
initialize a group
update(c, cwnd, sshthresh, state);
returns: cwnd, ssthresh, state
Update
Leave(c)
Leave
Remove entry from the list
If last conn: delete group

## Slide 11: Changes in the TCP code
register(c, p, cwnd, sshtresh);
returns: cwnd, ssthresh, state
update(c, cwnd, sshthresh, state); returns: cwnd, ssthresh, state
leave(c)
Initialization: executed at the beginning of the session!
Update: executed whenever a TCP session newly calculates its cwnd
Leave: executed whenever a TCP session is terminated

## Slide 12: Evaluation
Implementation
  FreeBSD 11 kernel with state shared across the freely available VirtualBox hypervisor
  ns-2 simulator
the source code is available at: http://safiquli.at.ifi.uio.no/tcp-ccc/
Fairness between two VMs, with 1 flow in VM1 and 1 to 4 flows in VM2 across a 10Mbit/s⇥100ms bottleneck

## Slide 13: Applicability of simulation results
Datacenter | Internet | BDP (1500 byte packets)
10 Gbit/s, 100 μs [1] | 10 Mbit/s, 100 ms | 83.3
10 Gbit/s, 10..100 μs: [2] | 1..10 Mbit/s, 100 ms | 8.3 .. 83.3
1 Gbit/s, 100 μs: [3] | 10 Mbit/s, 10 ms | 8.3
1 Gbit/s, 250 μs: [4] | 25 Mbit/s, 100 ms | 208.3
Referenced datacenter conditions are comparable to common Internet bandwidth X delay products
[1] M. Alizadeh, A. Greenberg, D. A. Maltz, J. Padhye, P. Patel, B. Prabhakar, S. Sengupta, and M. Sridharan, “Data Center TCP (DCTCP),” ACM SIGCOMM, 2010
[2] R. Mittal, V. T. Lam, N. Dukkipati, E. Blem, H. Wassel, M. Ghobadi, A. Vahdat, Y. Wang, D. Wetherall, and D. Zats, “Timely: Rtt-based congestion control for the datacenter,” ACM SIGCOMM, 2015.
[3] A. M. Abdelmoniem, B. Bensaou, and A. J. Abu, “HyGenICC: Hypervisor-based generic IP congestion control for virtualized data centers,” IEEE ICC, May 2016
[4] A. Munir, G. Baig, S. M. Irteza, I. A. Qazi, A. X. Liu, and F. R. Dogar, “Friends, not foes: Synthesizing existing transport strategies for data center networks,” ACM SIGCOMM, 2014

## Slide 14: Results – mean Q length and loss ratio
Mean queue length and loss ratio as the RTT ratios between 2 flows is varied
minRTT 20ms, maxRTT 200ms, Bottleneck: 10Mb, preprocessed TMIX background Traffic (taken from 60 minute trace of campus traffic of university of north Carolina – approximate load 50%, RTT of the background traffic 80-100ms)

## Slide 15: Results – flow completion time
Flow completion time (FCT) of a short flow, with and without ctrlTCP
Long Flow – 25 Mb, short flow - 200KB, capacity varied from 1 to 10 Mb

## Slide 16: Conclusion
Allows datacenter administrators to exert precise control over the relative bandwidth share offered to coupled flows, with only minimal interfacing to the kernel TCP code
Implementation in the FreeBSD kernel and ns2 simulator
Works with flows with heterogeneous RTTs
Eliminates competition and reduces flow completion time
Future work:
  by changing the increase/decrease behavior as a function of the number of flows in a coupled group
  to investigate our solution on 10Gbps links while considering typical practical challenges at high speeds such as CPU delay

## Slide 17: Thank you!
Questions?